## Slide 1
C12 HACKATHON / REFERENCE SOLUTION
AUTOMATE CSD CALIBRATION
Detect the sticks. Measure their contrast. Recenter as the barriers move the scene.
A physics-guided detector + a drift-aware global optimizer
01
DETECT
short dark sticks
02
QUANTIFY
local contrast
03
RECENTER
plunger plane
10 MIN · ENGLISH · REPRODUCIBLE SEEDS

## Slide 2
01 / DETECTION
A sparse target inside a noisy map
C12 / 02
MEASURE · INFER · TUNE
WHAT COUNTS AS A STICK?
•
Short and dark
•
Near 45° orientation
•
Only a few pixels wide
Row stripes and long charging-line connectors are nuisance structure, not labels.
Raw CSD → ground truth → detector overlay

## Slide 3
01 / DETECTION
Matched filters grounded in device geometry
C12 / 03
MEASURE · INFER · TUNE
1
ROW BASELINE
Subtract each row's median to suppress shared horizontal noise.
→
2
TEMPLATE BANK
Blurred, zero-sum dark rectangles across physical length, width, and angle.
→
3
MASK
Noise-normalized response → non-maximum suppression → winning footprint.
WHY THIS MODEL?
Known geometry is a transferable prior; no training-set leakage, metadata input, or image normalization.
Segmentation threshold fixed at 4.0 on validation seed 999.

## Slide 4
01 / VALIDATION
Held-out detection: high recall, transparent trade-off
C12 / 04
MEASURE · INFER · TUNE
120
held-out images seed 2026
PIXEL MASK
0.746
macro F1
0.608
macro IoU
OBJECT-LEVEL
0.931
stick recall
0.718
object precision
Validation: 100 images / seed 999 · Test threshold untouched · 8-connected overlap defines an object hit

## Slide 5
02 / OBJECTIVE
Optimize the strongest interdot, not image standard deviation
C12 / 05
MEASURE · INFER · TUNE
THE FIVE GATES
g1 · g3 · g5
barriers: contrast + drift
g2 · g4
plungers: recenter the scan
MEASUREMENT OBJECTIVE
strongest local dip
matched response ÷ template gain
Removes most pixel-area bias while avoiding scene-wide dilution.
Objective uses measured images only.

## Slide 6
02 / TRACKING
Drift correction is part of the experiment
C12 / 06
MEASURE · INFER · TUNE
BARRIER STEP
gates change
→
IMAGE SHIFT
sticks move
→
REGISTER EDGES
estimate Δx, Δy
→
PAN WINDOW
keep sticks visible
CALIBRATE
6 orthogonal probes
FIT
robust linear → quadratic drift
GUARD
ambiguous match → repeat + average
Relative registration only: no known drift matrix, reveal(), or simulator attributes.

## Slide 7
02 / SEARCH
Global exploration → local pattern search
C12 / 07
MEASURE · INFER · TUNE
01 GLOBAL
48 scrambled Sobol points
3-D barrier cube: [−0.5, 0.5]³
Trackable route
Nearest-neighbour order; each barrier move ≤ 0.08 V. Intermediate measurements still contribute scores.
02 LOCAL
Two separated starts
0.08 V
explore
→
0.04 V
refine
→
0.02 V
refine
→
0.01 V
confirm
Coordinate pattern search · 2 frames for local comparisons · 3-frame final score

## Slide 8
02 / RESULTS
Ten fresh devices: strong measured-score recovery
C12 / 08
MEASURE · INFER · TUNE
0.874
mean score ratio
0.857
median ratio
334.5 scans 7.53M pixels median budget
Oracle measurements are post-run self-checks and excluded from the optimizer budget. Ratios are noisy image-derived proxies.

## Slide 9
03 / OUTLOOK
What transfers — and what we would improve next
C12 / 09
MEASURE · INFER · TUNE
TRANSFER
Physical template prior Row-noise suppression Fixed-seed evaluation
LIMITS
Known stick geometry Ambiguous low-SNR drift Noisy strongest-stick estimate
NEXT
Uncertainty-aware CNR Multi-resolution scans Bayesian / trust-region search
TAKE-AWAY
Build the objective from physics. Track the scene. Keep the oracle outside the algorithm.